Installing the LLCF modules

Requirements :

Knoppix 3.7 (Kernel 2.4.27) with include path =
/usr/src/linux/include,
check if this is present or not.
hint : the name linux is the symbolic link to the actual kernel directory ( in this case linux-2.4.27 )
Hardware : i386 architecture

cat /proc/version – should be Linux version 2.4.27
locate autoconf.h or ( /usr/src/linux-2.4.27/include/linux/autoconf.h)
cat /usr/src/linux-2.4.27/include/linux/autoconf.h | grep CONFIG_KMOD
must be 1
cat /usr/src/linux-2.4.27/include/linux/autoconf.h | grep CONFIG_PROC_FS
must be 1

The include data must be “used from” /usr/src/linux/include and not in /usr/include/linux

In the make file the CC and the source directory of linux is mentioned. But if you want to change it during the make we will have to give parameters as below :

make CC=gcc-2.95 KERNELDIR=/usr/src/linux-2.4.26
if you want to use the Debug facility:
make CC=gcc-2.95 KERNELDIR=/usr/src/linux-2.4.26 DEBUG=-DDEBUG
- Copy all the files under a directory , for eg. /home/guitar/llcf
- make a directory 'llcf' under /lib/modules/2.4.27/
- copy /boot/System.map file to /usr/src/linux/
- cd /home/guitar/llcf
- enter the src directory
Command	Action
make clean	Deletes all the object files created in the /home/guitar/llcf/src directory
Make all	Creates object files / can.o , vcan.o, can-bcm.o, can-raw.o
Make all-vw	Creates object files / can-tpgen.o, can-tp20.o, can-tp16.o, can-mcnet.o
Make install	Copies the object files created by 'make all' to / /lib/modules/2.4.27/llcf/ and changes the read write permission. / Checks for module dependancy conflict. This should not give any error.
Make install-vw	Copies the object files created by 'make all-vw' to / /lib/modules/2.4.27/llcf/ and changes the read write permission. / Checks for module dependancy conflict. This should not give any error.
Depmod -a	Checks dependancy
Change directory to /home/guitar/llcf/src/test
Make clean / Make all / make all-vw	Creates all the test programs

Installing the PEAK Driver

Requirements

PEAK CAN USB Hardware
Can controller : SJA1000
CAN transciever : PCA82C251

Please do not use the drivers provided by peak as they do not contain the network device support.
- Copy the modified drivers for peak into /home/guitar/llcf/peak
- go to the driver directory
- create a directory /usr/local/bin

Command	Action
Change to directory driver
Make clean / make all	Creates the object files / pcan_main, pcan_fops, pcan_pci, pcan_isa, pcan_dongle, pcan_fifo, pcan_sja1000, pcan_parse, pcan_netdev, pcan_usb, pcan_usb_kernel_org
Make install	Copies pcan.o into / /lib/modules/2.4.27/misc/ / copies pcan.h to /usr/include/ directory / pcan_make_devices is made a /sbin command ( can be called from anywhere in the shell )
Change directory /home/guitar/llcf/peak/lib
Make clean / make all	Creates object file libpcan.so.0.3 / ( necessary for run time linking.. for test programmes specific to Peak )
Make install	Copies libpcan.so.0.3 to /usr/lib/ / Necessary links and cache created for the above file
Ls -l /usr/lib/libpcan* / lrwxrwxrwx 1 root root 21 Apr 19 05:53 libpcan.so -> /usr/lib/libpcan.so.0 / lrwxrwxrwx 1 root root 23 Apr 19 05:53 libpcan.so.0 -> /usr/lib/libpcan.so.0.3 / -rwxr-xr-x 1 root root 12260 Apr 19 05:53 libpcan.so.0.3
Insmod pcan	Check by seeing lsmod, it should appear as / pcan / usbcore [pcan usb-storage usb-ohci]
pcan_make_devices 1	Would create devices for each interface : pci, isa, epp, sp, usb
Ls /dev/pcan*	/dev/pcan0 /dev/pcan16 /dev/pcan24 /dev/pcan32 /dev/pcan8
Cat /proc/pcan / *--------- PEAK-Systems CAN interfaces (www.peak-system.com) ----------- / *----------------------- release_20050212_u -------------------------- / *------------------ 1 interfaces @ major 254 found --------------------- / *---------- netdevice support 2006-03-10 16:52 for LLCF v1.0.0 --------- / *n typ ndev ---base--- irq --btr- --read-- --write- --irqs-- --error- status / 32 usb can0 0xffffffff 255 0x001c 00000000 00000000 0000120a 000010bc 0x000c / The others ( pci, isa, epp, sp ) are not visible because no peak hardware is connected to those ports.

Installation over :). The next time when the computer is started the pcan module is loaded and unloaded depending on the presence of the hardware in the usb port.

Inserting Modules and ifconfig ( can also be done automatically )

- Start the computer with / without the peak hardware
- plug the Peak USB hardware in the USB port if not done before.
insmod can / insmod vcan / insmod can-raw / insmod can-bcm / insmod can-tpgen / insmod can-tp2 / shell – script = load_modules.sh / ( please only do this in the above order ) / can-bcm 8872 0 (unused) / can-raw 3492 0 (unused) / can-tp20 7300 0 (unused) / can-tpgen 5928 0 [can-tp20] / vcan 2624 1 / can 19612 0 [can-bcm can-raw can-tp20 can-tpgen]
Echo "i 0x4914 s" > /dev/pcan32 / put this line also in load_modules.sh.	Changes the default bit rate of 500kbps to 100kbps / others are / 0x4914 100kbps / 0x4114 500kbps / 0x4014 1000kbps
Ifconfig can0 up / ifconfig vcan2 up	To enable the network ports.
ifconfig / can0 Link encap:UNSPEC HWaddr 00-00-00-00-00-00-00-00-00-00-00-00-00-00-00-00 / UP RUNNING NOARP MTU:8 Metric:1 / RX packets:0 errors:0 dropped:0 overruns:0 frame:0 / TX packets:18 errors:2 dropped:0 overruns:0 carrier:0 / collisions:0 txqueuelen:10 / RX bytes:0 (0.0 b) TX bytes:104 (104.0 b) / eth0 Link encap:Ethernet HWaddr 00:13:8F:15:35:9E / inet addr:192.168.111.100 Bcast:192.168.111.255 Mask:255.255.255.0 / UP BROADCAST RUNNING MULTICAST MTU:1500 Metric:1 / RX packets:4034 errors:0 dropped:0 overruns:0 frame:0 / TX packets:1452 errors:0 dropped:0 overruns:0 carrier:0 / collisions:0 txqueuelen:1000 / RX bytes:911138 (889.7 KiB) TX bytes:294472 (287.5 KiB) / Interrupt:19 Base address:0xd400 / lo Link encap:Local Loopback / inet addr:127.0.0.1 Mask:255.0.0.0 / UP LOOPBACK RUNNING MTU:16436 Metric:1 / RX packets:51 errors:0 dropped:0 overruns:0 frame:0 / TX packets:51 errors:0 dropped:0 overruns:0 carrier:0 / collisions:0 txqueuelen:0 / RX bytes:3483 (3.4 KiB) TX bytes:3483 (3.4 KiB) / vcan2 Link encap:Local Loopback / UP LOOPBACK RUNNING MTU:14 Metric:1 / RX packets:6391 errors:0 dropped:0 overruns:0 frame:0 / TX packets:6391 errors:0 dropped:0 overruns:0 carrier:0 / collisions:0 txqueuelen:1000 / RX bytes:102256 (99.8 KiB) TX bytes:102256 (99.8 KiB)

Running the test programmes

The test programmes are configured only for vcan2
- change to directory /home/guitar/llcf/src/test/
- open 4 shells

RAW interface testing

Shell 1 :
watch cat /proc/sys/net/can/rcvlist_*

Shell 2 :
./canecho vcan2

Shell 3:

./candump vcan2

Shell 4 :

invoke a send frame ; ./tst-raw-sendto

The above test tests communication on can-raw interface, because the canecho reflects the send data via tst-raw-sendto and which can be seen in candump.

BCM testing

use the same procedure as above

Shell 5 : in addition open another shell and run ./can-sniffer vcan2

The bcm datas / cycles can be seen on the watch window.

TP20 interface testing

Shell 3:

./candump vcan2

Shell 4:

./tp20-server
and wait for the client

Shell 5:
./tp20-client

The handshake and data exchange can be seen on the candump.

In all cases above if the real hardware is to be used then a new executable has to be created with the hardcoded value
only for test purposes
#define DEV "can0" instead of #define DEV "xxx"

tp20-server and tp20-client

 vcan2 200 [7] 01 C0 00 10 21 03 20
 vcan2 201 [7] 00 D0 21 03 42 02 20
 vcan2 242 [6] A0 0F CA FF 00 FF
 vcan2 321 [6] A1 0F CA FF 00 FF
 vcan2 242 [8] 20 65 69 6E 6E 65 67 65
 vcan2 242 [8] 21 72 6D 69 74 67 61 7A
 vcan2 242 [8] 22 65 6C 6C 65 7A 61 67
 vcan2 242 [8] 23 74 69 6D 72 65 67 65
 vcan2 242 [5] 14 6E 6E 69 65
 vcan2 321 [1] B5
 vcan2 321 [8] 20 45 49 4E 4E 45 47 45
 vcan2 321 [8] 21 52 4D 49 54 47 41 5A
 vcan2 321 [8] 22 45 4C 4C 45 5A 41 47
 vcan2 321 [8] 23 54 49 4D 52 45 47 45
 vcan2 321 [5] 14 4E 4E 49 45
 vcan2 242 [1] B5
 vcan2 242 [1] A8
 vcan2 321 [1] A8

Python

On Debian Linux, 'distutils' is not installed with package
'python2.3'. You should install 'python2.3-dev'

install python2.4

Download python2.4
http://www.python.org/download/releases/2.4/

Python-2.4.tar.bz2

The tar.bz2 is considerably smaller, so get that one if your system has the appropriate tools to deal with it. Unpack it with
tar -zxvf Python-2.4.tgz (or bzcat Python-2.4.tar.bz2 | tar -xf -).

Change to the Python-2.4 directory and run the "./configure", "make", "make install" commands to compile and install Python. The source archive is also suitable for Windows users who feel the need to build their own version.

Auto complete:
http://www.network-theory.co.uk/docs/pytut/tut_84.html

Add auto-completion and a stored history file of commands to your Python interactive interpreter. Requires Python 2.0+, readline. Autocomplete is bound to the Esc key by default (you can change it - see readline docs).# Store the file in ~/.pystartup, and set an environment variable to point to it: "export PYTHONSTARTUP=/home/guitar/.pystartup" in bash.

http://www.codecoffee.com/tipsforlinux/articles/030.html

Note that PYTHONSTARTUP does *not* expand "~", so you have to put in the full path to your home directory.

Save the below file with name .pystartup in put it in the location as dscribed by PYTHONSTARTUP
import atexit
import os
import readline
import rlcompleter

readline.parse_and_bind('tab: complete')
historyPath = os.path.expanduser("~/.pyhistory")

def save_history(historyPath=historyPath):
    import readline
    readline.write_history_file(historyPath)

if os.path.exists(historyPath):
    readline.read_history_file(historyPath)

atexit.register(save_history)
del os, atexit, readline, rlcompleter, save_history, historyPath
>>> import sys
>>> sys.path
['', '/usr/local/lib/python2.3', '/usr/local/lib/python2.3/plat-linux2',
 '/usr/local/lib/python2.3/lib-tk', '/usr/local/lib/python2.3/lib-dynload',
 '/usr/local/lib/python2.3/site-packages']
>>>
open .bashrc in the home directory and make the following changes.
PYTHONSTARTUP="/home/guitar/.pystartup"
export PYTHONSTARTUP

> > > > Try hitting control-r and typing a short string that last appeared
> > > > in the line desired ("my" or even "m" would work in this case).
Make a symbolic link to the build directory.

Channel on which u can discuss about python is freenode in IRC

knoppix / configure / printer

printer : 192.168.111.107
port : IP_192.168.111.107
Brother MFC-9050 driver
name : Brother-MFC8840D

tail -f -n1000 test.txt

put the files can.h, bcm.h, raw.h, af_can.h in the current directory.
On the console command: python setup.py build

Create a symbolic link _llcf.so
ln -s build/lib.linux-i686-2.4/_llcf.so ../_llcf.so

Follow the code to open, close sockets.
Follow the code to send recieve messages.

# *
# * Process.txt
# *
# * Copyright (c) 2002-2005 Schefenacker Innovation GmBH, Germany
# * All rights reserved.
# *
# *
# * Send feedback to <vikas.agrawal@web.de>
#
# ****************************************************************************
# * Process.txt - Description for the different modules
# *
# * $Id: Process.txt 2006-08-28 ( yy-mm-dd) agrawal $
# ****************************************************************************
# *
# * Description for the different modules
# * $Log: Process.txt,v $
# * Revision 1.0 2006/08/28 22:03:29 agrawal
# * Initial Revision
# *
# *****************************************************************************
in .bashrc.
PYTHONSTARTUP=/home/guitar/.pystartup"
export PYTHONSTARTUP
Save the file pystartup with name .pystartup in put it in the location as dscribed by PYTHONSTARTUP
Copy the entire folder ( Delivery ) to a location
run the script systempathappend.py to add the path to the Pythonypath ( Caution with unix and windows )
--------------------------
User Files:
candump.py = start the candump to view the messages on the can bus
        import candump or reload(candump)
        all the messages on the CAN bus wud be immediately visible
EMC_check.py = file for ping pong of CAN message between the Fujitsu for electromagnetic check at EMC...
        import EMC_check or reload(EMC_check)
        EMC_check.send_raw()
        the messages are sent and recieved. On non recieve of message in desired time, a error signal is written into a log file with a time stamp.
create a socket : socket = llcf.SOCKET()
create a frame : frame = llcf.FRAME()
socket.send(f), socket.recv(), socket.close()
recv structure:
recv_frame = socket.recv()
recv_frame[0] = CANID
recv_frame[1] = DLC
recv_frame[2] = 'can0' or relevant sockets
recv_frame[3] = array of Datas
------------------------
LogFiles:
dump.txt - a file created by invoking candump. Achtung ! , the file is overwritten with the next import / reload of candump
--------------------------
System Files:
llcfmodule.c = an extension module to wrap the LLCF drivers.
llcf.py = for llcf functionality please import the file in the user script
---------------------------